## Slide 1: Introduction to ATM
Copyright, 1998 © David J. Young
technologies
Collective
a pencom company
David J. Young
Collective Technologies
25-August-1998

## Slide 2: Introduction
This talk is a basic introduction to ATM technology. We will introduce the key concepts of ATM technology, present ATM terminology such as LAN Emulation (LANE), Classical IP, Virtual LANs (VLANs), and Quality of Service (QoS). Finally, the Pros and Cons of ATM networks are presented to give a basic understanding of TCP/IP LANs built using ATM.

## Slide 3: What is ATM?
“Asynchronous Transfer Mode is a communications networking technology that carries information in 53-byte chunks known as cells”

## Slide 4: ATM Reference Model
ATM is independent of any specific transmission medium
ATM layer defines cell format, how cells are transported, and how to treat congestion. It also defines virtual circuit creation and termination.
ATM adaptation layer defines the process of converting information from upper layers into ATM cells.
ATM adaptation layer (AAL)
Physical layer
ATM layer
Services and applications
Network
Physical
Datalink
Transport
ATM layers
OSI layers

## Slide 5: Physical Layer
Industry experts endorse SONET for both LAN and WAN
ATM Forum recommends FDDI (100Mb/s), Fibre Channel (155Mb/s), OC3 (155Mb/s) and T3 (45Mb/s)
Most carriers are providing T3 links to their ATM networks

## Slide 6: ATM Layer
Defines structure of the ATM cell
  UNI (User Network Interface)
  NNI (Network-to-Network Interface)
Defines virtual channel and path routing
  Cell address translation
  Cell header generation/removal
Transmission/Switching/Reception
Congestion Control/Buffer Management
Sequential delivery

## Slide 7: ATM Cell
Fixed cell size
Overhead is ~10%
Able to time the flow of cells
Cell switching is fast & efficient
Traffic flow is predictable
Can guarantee time-sensitive info
NNI cell does not have GFC field
Payload
Hdr
48-bytes
5-bytes
GFC Generic Flow Control
VPI Virtual Path Identifier
VCI Virtual Channel Identifier
PTI Payload Type Indicator
RES Reserved
CLP Cell Loss Priority
HEC Header Error Control
GFC
VPI
VPI
VCI
VCI
VCI
PTI
RES
CLP
HEC

## Slide 8: Frame vs Cell
Frames are variable length
ATM cells are always 53-bytes
time

## Slide 9: ATM Adaptation Layer
Adaptation defines how higher-layer information such as voice, data and video are inserted into the payload of the 53-byte ATM cells

## Slide 10: AAL Service Types
Type 1: A connection-oriented CBR (constant bit rate) service with timing for audio and video applications
Type 2: A connection-oriented VBR (variable bit rate) service for real-time applications where minor loss is acceptable, and for non-real-time VBR, such as transaction processing
Type 3/4: An ABR (available bit rate) service for non-time-critical applications such as LAN internetworking and LAN emulation
Type 5: A UBR (unspecified bit rate) service that provides spare bandwidth to noncritical services such as file transfers

## Slide 11: ATM Service Classes
Class A
Class B
Class C
Class D
Type 1
Type 2
Type 3/4
Type 5
Type 3/4
Connection-oriented
Connectionless
Requires Timing
Timing not required
Constant
bit rate
Variable bit rate

## Slide 12: Virtual Connections
ATM is connection-oriented
Connections are bidirectional and full duplex
Two types of VCs
  Virtual Channel Connection (VCC)
    Logical connections between end stations
  Virtual Path Connection (PVC)
    A bundle of Virtual Channels (VCCs)

## Slide 13: Virtual Paths & Channels
Virtual Paths
VCI-1
VCI-2
VCI-3
VCI-1
VCI-2
VCI-1
VCI-2
VCI-1
VCI-2
VCI-3
VPI-1
VPI-2
VPI-3
VPI-4
VPI-5
VPI-6

## Slide 14: Virtual Circuits
Two types of virtual circuits
  Permanent Virtual Circuit (PVC)
    A VCC or VPC that is predefined and left in place all the time. If information is not being transmitted, it doesn’t use any bandwidth
  Switched Virtual Circuit (SVC)
    A VCC that is setup at the instant that information needs to be sent between communication endpoints, and then taken down after the transmission is finished

## Slide 15: ATM Interfaces
UNI (User Network Interface)
  Defines the connection between user equipment and ATM equipment (e.g. a workstation and the ATM switch)
NNI (Network-to-Network Interface)
  The interface between ATM devices
ICI (Intercarrier Interface)
  The interface between different ATM carriers
DXI (Data Exchange Interface)
  Interface from ATM into legacy equipment (such as routers into ATM using HDLC)

## Slide 16: ATM Interfaces

## Slide 17: ATM for LANs
IP LANs are connectionless
ATM is connection-oriented
Can you integrate the two?

## Slide 18: A Look at IP
When one station transmits, all stations hear the message, but only the station to which the message is addressed responds (one-to-one)
Broadcasts are transmitted to all stations (one-to-many)
IP networks use ARP to determine which circuit to use when sending a message
IP is stateless

## Slide 19: A Look at ATM
ATM sets up virtual circuites between endpoints (one-to-one)
ATM does not support broadcasts
ATM is state-full

## Slide 20: IP-over-ATM
Encapsulation (RFC-1483)
Classic IP (RFC-1577)
LAN Emulation (LANE)
MultiProtocol Over ATM (MPOA)

## Slide 21: Encapsulation
RFC-1483 is Multiprotocol Encapsulation over ATM
Generally used for WANs
Two encapsulation methods supported:
  LLC/SNAP (Logical Link Control/Sub-Network Access Protocol)
    A single connection to support multiple packet types
  VC multiplexing
    carries a single protocol

## Slide 22: Classical IP
Analogous to Ethernet MAC
Uses ATM as a high-speed backbone
A VCI for a “virtual wire” is used for cell transmission
Implements the concept of a LIS (Logical IP subnet)
Each LIS includes a ATMARP server (resolves IP to ATM addresses)
Must use a “one armed” router to communicate with hosts in another LIS

## Slide 23: Classical IP Network

## Slide 24: LAN Emulation
A method to connect legacy LANs to ATM
LANE provides translation services between:
  variable length frames on shared connectionless networks
  fixed length, connection-oriented networks with virtual circuits

## Slide 25: LANE Components
LEC (LAN Emulation Client)
  devices that run LANE software to perform translation between legacy LANs and ATM
LES (LAN Emulation Server)
  resolves legacy LAN (MAC) addresses to ATM addresses within the ELAN (Emulated LAN)

## Slide 26: LANE Components
LECS (LAN Emulation Configuration Server)
  Not to be confused with LECs
  Responsible for assigning, managing and tracking membership of LECs in ELANs
BUS (Broadcast and Unknown Server)
  Simulates the broadcast and multicast functions normally present on shared LANs by sending messages individually to all devices in an ELAN

## Slide 27: LANE Network

## Slide 28: LANE Summary
Basically creates a bridged LAN network across the ATM fabric
To send data to another system, a workstation only needs to know the MAC address of the destination system
LANE handles the ATM addressing and virtual circuit connections (LEC)
LECs request MAC-to-ATM address resolution from the LES
Routers are required to move packets from one ELAN to another
LANE “hides” ATM from applications
IP has no way to talk to the network to specify QoS

## Slide 29: MPOA
Requires LANE
Takes advantage of ATM switching speeds
Allows end devices attached to ATM to communicate directly instead of through a router
Uses NHRP (Next Hop Routing Protocol) to establish a “cut-through” route to the destination
Clients use LANE to resolve addresses within the same Virtual LAN (VLAN)
Use MPOA for inter-VLAN addressing
LANE is for layer 2 switching
MPOA effectively performs layer 3 switching
MPOA can use ATM’s QoS

## Slide 30: Virtual LANs
A LAN is a broadcast domain; you know them as “subnets”
Switched networks are flat, i.e. one broadcast domain
Virtual LANs are “logical” groupings of machines to form subnets in switched networks

## Slide 31: VLANs
VLANs can be based on:
  Switch port address
  MAC address
  IP address
  IP multicast
  Protocol Type
  Policy or rules

## Slide 32: Quality of Service
AAL service categories:
  CBR, VBR-RT, VBR-nRT, ABR, UBR
Bandwidth attributes:
  Peak Cell Rate (PCR)
  Cell Delay Variation Tolerance (CDVT)
  Sustained Cell Rate (SCR)
  Minimum Cell Rate (MCR)
  Maximum Burst Size (MBS)
  Cell Loss Ratio (CLR)
  Cell Transfer Delay (CTD)

## Slide 33: ATM’s Benefits
Data, Voice, Video Integration
Seamless (LAN, MAN, WAN)
QoS (Quality of Service)
Automatic Load Balancing
Automatic Failover
Fast and Efficient
Highly Scalable

## Slide 34: ATM’s Drawbacks
Cost
Lack of exposure
Standards are still evolving
IP applications can’t talk to the network
Requires emulation to integrate with legacy LANs

## Slide 35: Summary
Excellent technology for backbone networks
Integrates well with other WAN & LAN technologies
Can combine corporate voice and data networks for economics
Not appropriate in all situations
Requires a significant amount of time & expertise for implementation, maintenance & on-going operation

## Slide 36: Contact
<http: //www.uniforum.chi.il.us>
<mailto: davidy@colltech.com>
<phone: 312-781-6200>